## Slide 1: Building Arduino Applications
Dr. Abdelhameed Ibrahim Assoc. Prof. Computer Engineering

## Slide 2: Day 1
Welcome to the course!
During Day 1,
We are going to introduce you to the course.
How to assemble a circuit on a breadboard circuit?
Let us get acquainted with Arduino
Development tools for Arduino IDE
First glance at a program
First coded material
Macro definitions, variables, counting loops.

## Slide 3: Arduino Uno

## Slide 4: Board Breakdown
Here are the components that make up an Arduino board and what each of their functions are:
Reset Button – This will restart any code that is loaded to the Arduino board.
AREF – Stands for “Analog Reference” and is used to set an external reference voltage
Ground Pin – There are a few ground pins on the Arduino and they all work the same
Digital Input/Output – Pins 0-13 can be used for digital input or output
PWM – The pins marked with the (~) symbol can simulate analog output
USB Connection – Used for powering up your Arduino and uploading sketches
TX/RX – Transmit and receive data indication LEDs

## Slide 5: Board Breakdown
8. ATmega Microcontroller – This is the brains and is where the programs are stored
9. Power LED Indicator – This LED lights up anytime the board is plugged in a power source
10. Voltage Regulator – This controls the amount of voltage going into the Arduino board
11. DC Power Barrel Jack – This is used for powering your Arduino with a power supply
12. 3.3V Pin – This pin supplies 3.3 volts of power to your projects
13. 5V Pin – This pin supplies 5 volts of power to your projects
14. Ground Pins – There are a few ground pins on the Arduino
15. Analog Pins – These pins can read the signal from an analog sensor and convert it to digital

## Slide 6: Types of Arduino Boards

## Slide 7: How To Program Arduino
https://www.arduino.cc/
https://code.visualstudio.com/
https://www.tinkercad.com/dashboard
https://www.sites.google.com/site/unoardusim/services

## Slide 8: List of experiments
TUTORIALS > Built-In Examples > 01.Basics > Blink
TUTORIALS > Built-In Examples > 03.Analog > Fading

## Slide 9
What’s a Breadboard?

## Slide 10
TUTORIALS > Built-In Examples > 02.Digital > Button
TUTORIALS > Built-In Examples > 02.Digital > StateChangeDetection

## Slide 11: TUTORIALS > Built-In Examples > 05.Control > ForLoopIteration

## Slide 12: Day 2
It’s time to learn how to receive data with the help of sensors.
During Day 2,
First sensor
How to read off analog signals
Reading off digital signals
Boolean expressions and program branching
Seven-segment display
Usage of modules and RGB sensor
Joystick app and testing

## Slide 13: List of experiments
TUTORIALS > Built-In Examples > 03.Analog > AnalogInput

## Slide 14
Joystick Control
Code: Lesson 12 Analog Joystick Module
https://github.com/afai79/Arduino/blob/main/Books/Elegoo.zip

## Slide 15
Joystick Control
Code: Lesson 12 Analog Joystick Module
https://github.com/afai79/Arduino/blob/main/Books/Elegoo.zip

## Slide 16
7 Segment
https://github.com/afai79/Arduino/blob/main/7_segment.ino

## Slide 17
Four Digital Seven Segment Display

## Slide 18
https://github.com/afai79/Arduino/blob/main/4_digit_7_segment.ino

## Slide 19
Tone Melody
https://www.arduino.cc/en/Tutorial/BuiltInExamples/toneMelody
https://github.com/afai79/Arduino/blob/main/Lib/pitches.zip

## Slide 20
RGB sensor
Code: Lesson 4 RGB LED
https://github.com/afai79/Arduino/blob/main/Books/Elegoo.zip

## Slide 21: Day 3
Having learnt to create a step motor, you can create devices which can perform very precise actions. It could as well be just messing with your hand with which you are trying to control it.
During Day 3,
Servo and the library
Ultrasonic Sensor
LCD
Temperature and humidity sensor
Water level Sensor
Step motor
Motor control expansion board
LCD with I2C

## Slide 22
Servo motor control
Code: Lesson 9 Servo
https://github.com/afai79/Arduino/blob/main/Books/Elegoo.zip

## Slide 23
Ultrasonic Sensor

## Slide 24
Ultrasonic Sensor
https://github.com/afai79/Arduino/blob/main/Ultrasonic.ino

## Slide 25
PIR Sensor
https://github.com/afai79/Arduino/blob/main/PIR_Sensor.ino

## Slide 26
https://github.com/afai79/Arduino/blob/main/LCD.ino
LCD

## Slide 27: List of experiments
Temperature and humidity sensor.
Code: Lesson 11 DHT11 Temperature and Humidity Sensor
https://github.com/afai79/Arduino/blob/main/Books/Elegoo.zip

## Slide 28
Water level Sensor
https://www.thegeekpub.com/236571/arduino-water-level-sensor-tutorial/
https://github.com/afai79/Arduino/blob/main/water_level.ino

## Slide 29
Stepper motor
Code: Lesson 23 Stepper Motor
https://github.com/afai79/Arduino/blob/main/Books/Elegoo.zip

## Slide 30
LCD with I2C
https://github.com/afai79/Arduino/blob/main/LCD_I2C.ino

## Slide 31: Day 4
Having learnt to use a lot of sensors and devices with Arduino
During Day 4, you are ready to make various small projects based on your skills.
Small Project 1: Air Quality Detector
Small Project 2: Control servo motor by RGB sensor
Small Project 3: Smart House
Small Project 4: BMA400 and MPU6050 sensors-based projects

## Slide 32: Small Project 1: Air Quality Detector
Gas Sensor

## Slide 34
https://github.com/afai79/Arduino/blob/main/Gas_sensor.ino
https://github.com/afai79/Arduino/blob/main/Gas_sensor-LED-Motor.ino

## Slide 35
https://github.com/afai79/Arduino/blob/main/Gas_Piezo.ino

## Slide 36: Small Project 2: Control servo motor by RGB sensor
https://github.com/afai79/Arduino/blob/main/RGB_LED-motor.ino

## Slide 37: Small Project 3: Smart House
https://github.com/afai79/Arduino/blob/main/Ultrasonic_Servo_Gas_P.ino

## Slide 38: Small Project 4: BMA400 and MPU6050 sensors-based projects
Grove - 3-axis digital accelerometer ±16 g low power (BMA400)
PIN | DESCRIPTION
1. | SCL - clock line I2C
2. | SDA - I2C data line
3. | System power supply from 3.3 V to 5 V
4. | System weight
5. | BMA400 module

## Slide 39
https://github.com/afai79/Arduino/blob/main/Lib/BlueDot_BMA400_Library-1.0.0.zip
https://github.com/afai79/Arduino/blob/main/Lib/Grove_3Axis_Digital_Accelerometer_BMA400-master.zip

## Slide 40
MPU6050 Triple Axis Gyroscope & Accelerometer
https://github.com/afai79/Arduino/blob/main/Lib/Arduino-MPU6050-master.zip

## Slide 41: Day 5
Arduino Robot – An easy DIY project
  We are going to build an Arduino based robot capable of avoiding obstacles in its path.
  It is a fun project and a great learning experience, so without any further delay, let us get started!
https://educ8s.tv/arduino-robot-easy-diy-project/
https://github.com/afai79/Arduino/tree/main/ArduinoRobot

## Slide 42: Building the Robot
Step 1. Connect the motor and wheels to the chassis.

## Slide 43
Step 2: Prepare the Switch and connect the Power Source
Step 3: Mount other Parts on the chassis.

## Slide 44: Schematics
Wire up the components together as shown in the image below.

## Slide 45: Code
The code uses three libraries.
  Two of them must be downloaded for the program to compile.
  The first one is the motor shield driver from Adafruit.
  The second library is the NewPing library for the supersonic distance sensor.
https://github.com/afai79/Arduino/blob/main/ArduinoRobot/ArduinoRobot_.ino

## Slide 46: LIBRARIES
Motor Shield Library:
https://github.com/afai79/Arduino/blob/main/ArduinoRobot/Adafruit-Motor-Shield-library-master.zip
New Ping Library:
https://github.com/afai79/Arduino/blob/main/ArduinoRobot/NewPing_v1.9.1.zip

## Slide 47: End of Training!