## Slide 1: Building Arduino Applications
Dr. Abdelhameed Ibrahim Assoc. Prof. Computer Engineering

## Slide 2: Part 1
Welcome to the course!
During Day 1,
Introduction to the training course.
Know about Arduino
Learn how to assemble a circuit on a breadboard.
Development tools for Arduino IDE
First coded program
Macro definitions, variables, counting loops

## Slide 3: Arduino Uno

## Slide 4: Arduino Uno
Microcontroller | ATmega328P
Operating Voltage | 5V
Input Voltage (recommended) | 7-12V
Input Voltage (limit) | 6-20V
Digital I/O Pins | 14 (of which 6 provide PWM output)
PWM Digital I/O Pins | 6
Analog Input Pins | 6
DC Current per I/O Pin | 20 mA
DC Current for 3.3V Pin | 50 mA
Flash Memory | 32 KB (ATmega328P) of which 0.5 KB used by bootloader
Clock Speed | 16 MHz
LED_BUILTIN | 13
Length | 68.6 mm
Width | 53.4 mm
Weight | 25 g

## Slide 5: Arduino Board Breakdown
Reset Button –restart any code that is loaded to the Arduino board.
AREF – Stands for “Analog Reference” and is used to set an external reference voltage
Digital Input/Output – Pins 0-13 can be used for digital input or output
PWM – The pins marked with the (~) symbol can simulate analog output
USB Connection – Used for powering up your Arduino and uploading sketches
TX/RX – Transmit and receive data indication LEDs
ATmega Microcontroller – The brain and is where the programs are stored
Power LED Indicator –lights up anytime the board is plugged in a power source

## Slide 6: Arduino Board Breakdown
9. Voltage Regulator –controls amount of voltage going into Arduino board
10. DC Power Barrel Jack –used for powering the Arduino with a power supply
11. 3.3V Pin – This pin supplies 3.3 volts of power to your projects
12. 5V Pin – This pin supplies 5 volts of power to your projects
13. Ground Pins – There are a few ground pins on the Arduino
14. Analog Pins – These pins can read the signal from an analog sensor and convert it to digital

## Slide 7: Types of Arduino Boards

## Slide 8: How To Program Arduino
https://www.arduino.cc/
https://www.tinkercad.com/dashboard

## Slide 9: List of experiments
TUTORIALS > Built-In Examples > 01.Basics > Blink

## Slide 10
What’s a Breadboard?

## Slide 11
TUTORIALS > Built-In Examples > 02.Digital > Button

## Slide 12: TUTORIALS > Built-In Examples > 05.Control > ForLoopIteration

## Slide 13: Part 2
Learn how to receive data with the help of sensors.
First sensor
Reading off analog and digital signals
Joystick app and testing
Seven-segment display
Tone Melody
RGB sensor

## Slide 14: List of experiments
TUTORIALS > Built-In Examples > 03.Analog > AnalogInput

## Slide 15
Joystick Control
Code: Lesson 12 Analog Joystick Module
https://github.com/afai79/Arduino/blob/main/Books/Elegoo.zip

## Slide 16
Joystick Control
Code: Lesson 12 Analog Joystick Module
https://github.com/afai79/Arduino/blob/main/Books/Elegoo.zip

## Slide 17
7 Segment
https://github.com/afai79/Arduino/blob/main/7_segment.ino

## Slide 18
Four Digital Seven Segment Display

## Slide 19
https://github.com/afai79/Arduino/blob/main/4_digit_7_segment.ino

## Slide 20
Tone Melody
https://www.arduino.cc/en/Tutorial/BuiltInExamples/toneMelody
https://github.com/afai79/Arduino/blob/main/Lib/pitches.zip

## Slide 21
RGB sensor
Code: Lesson 4 RGB LED
https://github.com/afai79/Arduino/blob/main/Books/Elegoo.zip

## Slide 22: Part 3
Learn to create a step motor and create devices which can perform very precise actions.
Servo motor and libraries
Ultrasonic Sensor
PIR Sensor
LCD
LCD with I2C
Temperature sensor
Water level Sensor
Step motor

## Slide 23
Servo motor control
Code: Lesson 9 Servo
https://github.com/afai79/Arduino/blob/main/Books/Elegoo.zip

## Slide 24
Ultrasonic Sensor

## Slide 25
Ultrasonic Sensor
https://github.com/afai79/Arduino/blob/main/Ultrasonic.ino

## Slide 26
PIR Sensor
https://github.com/afai79/Arduino/blob/main/PIR_Sensor.ino

## Slide 27
https://github.com/afai79/Arduino/blob/main/LCD.ino
LCD

## Slide 28
LCD with I2C
https://github.com/afai79/Arduino/blob/main/LCD_I2C.ino

## Slide 29
Temperature sensor.
https://github.com/afai79/Arduino/blob/main/Temperature.ino

## Slide 30: List of experiments
Temperature and humidity sensor.
Code: Lesson 11 DHT11 Temperature and Humidity Sensor
https://github.com/afai79/Arduino/blob/main/Books/Elegoo.zip

## Slide 31
Water level Sensor
https://www.thegeekpub.com/236571/arduino-water-level-sensor-tutorial/
https://github.com/afai79/Arduino/blob/main/water_level.ino

## Slide 32
Stepper motor
Code: Lesson 23 Stepper Motor
https://github.com/afai79/Arduino/blob/main/Books/Elegoo.zip

## Slide 33: Part 4
Having learnt to use a lot of sensors and devices with Arduino
During Part 4, you are ready to make various small projects based on your skills.
Small Project 1: Air Quality Detector
Small Project 2: Control servo motor by RGB sensor
Small Project 3: Smart House

## Slide 34: Small Project 1: Air Quality Detector
Gas Sensor

## Slide 36
https://github.com/afai79/Arduino/blob/main/Gas_sensor.ino
https://github.com/afai79/Arduino/blob/main/Gas_sensor-LED-Motor.ino

## Slide 37
https://github.com/afai79/Arduino/blob/main/Gas_Piezo.ino

## Slide 38: Small Project 2: Control servo motor by RGB sensor
https://github.com/afai79/Arduino/blob/main/RGB_LED-motor.ino

## Slide 39: Small Project 3: Smart House
https://github.com/afai79/Arduino/blob/main/Ultrasonic_Servo_Gas_P.ino

## Slide 40: Part 5
Arduino Robot
  We are going to build an Arduino based robot capable of avoiding obstacles in its path.
  It is a great learning experience, let us get started!
https://educ8s.tv/arduino-robot-easy-diy-project/
https://github.com/afai79/Arduino/tree/main/ArduinoRobot

## Slide 41: Building the Robot
Step 1. Connect the motor and wheels to the chassis.

## Slide 42
Step 2: Prepare the Switch and connect the Power Source
Step 3: Mount other Parts on the chassis.

## Slide 43: Schematics
Wire up the components together as shown in the image below.

## Slide 44: Code
The code uses three libraries.
  Two of them must be downloaded for the program to compile.
  The first one is the motor shield driver from Adafruit.
  The second library is the NewPing library for the supersonic distance sensor.
https://github.com/afai79/Arduino/blob/main/ArduinoRobot/ArduinoRobot_.ino

## Slide 45: LIBRARIES
Motor Shield Library:
https://github.com/afai79/Arduino/blob/main/ArduinoRobot/Adafruit-Motor-Shield-library-master.zip
New Ping Library:
https://github.com/afai79/Arduino/blob/main/ArduinoRobot/NewPing_v1.9.1.zip

## Slide 46: End of Training!